## Slide 1: Specifications, Modeling, and Model of Computation
Jian-Jia Chen
(slides are based on Peter Marwedel)
TU Dortmund,
Informatik 12
2014年 10 月 08日
These slides use Microsoft clip arts. Microsoft copyright restrictions apply.
© Springer, 2010

## Slide 2: Hypothetical design flow
2: Specification
3: ES-hardware
4: System software (RTOS, middleware, …)
8. Test *
5: Evaluation & Validation (energy, cost, performance, …)
7: Optimization
6: Application mapping
Application Knowledge
Design repository
* Could be integrated into loop
Design
Numbers denote sequence of chapters

## Slide 3: Motivation for considering specs & models
  Why considering specs and models in detail?
  If something is wrong with the specs, then it will be difficult to get the design right, potentially wasting a lot of time.
  Typically, we work with models of the system under design (SUD)
  What is a model anyway?
time

## Slide 4: Models
Definition: A model is a simplification of another entity, which can be a physical thing or another model. The model contains exactly those characteristics and properties of the modeled entity that are relevant for a given task. A model
is minimal with respect to a task if it does not contain any other characteristics than those relevant for the task.
[Jantsch, 2004]:
Which requirements do we have for our models?

## Slide 5: Requirements for specification & modeling techniques: Hierarchy
Hierarchy Humans not capable to understand systems containing more than ~5 objects. Most actual systems require more objects  Hierarchy (+ abstraction)
  Behavioral hierarchy Examples: states, processes, procedures.
  Structural hierarchy Examples: processors, racks, printed circuit boards
proc
proc
proc

## Slide 6: Requirem. for specification & modeling techniques (2): Component-based design
  Systems must be designed from components
  Must be “easy” to derive behavior from behavior of subsystems
  Work of Sifakis, Thiele, Ernst, …
  Concurrency
  Synchronization and communication

## Slide 7: Requirements for specification & modeling techniques (3): Timing
  Timing behavior Essential for embedded and cy-phy systems!
    Additional information (periods, dependences, scenarios, use cases) welcome
    Also, the speed of the underlying platform must be known
    Far-reaching consequences for design processes!
“The lack of timing in the core abstraction (of computer science) is a flaw, from the perspective of embedded software” [Lee, 2005]

## Slide 8: Requirements for specification & modeling techniques (3): Timing (2)
4 types of timing specs required, according to Burns, 1990:
t
?
execute
Measure elapsed time Check, how much time has elapsed since last call
Means for delaying processes
t

## Slide 9: Requirements for specification & modeling techniques (3): Timing (3)
Possibility to specify timeouts Stay in a certain state a maximum time.
Methods for specifying deadlines Not available or in separate control file.
t
execute

## Slide 10: Specification of ES (4): Support for designing reactive systems
  State-oriented behavior Required for reactive systems; classical automata insufficient.
  Event-handling (external or internal events)
  Exception-oriented behavior Not acceptable to describe exceptions for every state
We will see, how all the arrows labeled k can be replaced by a single one.

## Slide 11: Requirements for specification & modeling techniques (5): More Features
  Presence of programming elements
  Executability (no algebraic specification)
  Support for the design of large systems ( OO)
  Domain-specific support
  Readability
  Portability and flexibility
  Termination
  Support for non-standard I/O devices
  Non-functional properties
  Support for the design of dependable systems
  No obstacles for efficient implementation
  Adequate model of computation What does it mean “to compute”?

## Slide 12: Problems with classical CS theory and von Neumann (thread) computing
Even the core … notion of “computable” is at odds with the requirements of embedded software.
In this notion, useful computation terminates, but termination is undecidable.
In embedded software, termination is failure, and yet to get predictable timing, subcomputations must decidably terminate.
What is needed is nearly a reinvention of computer science.
Edward A. Lee: Absolutely Positively on Time, IEEE Computer, July, 2005
  Search for non-thread-based, non-von-Neumann MoCs.

## Slide 13: Models of computation
What does it mean, “to compute”?
Models of computation define:
  Components and an execution model for computations for each component
  Communication model for exchange of information between components.
C-1
C-2

## Slide 14: Dependence graph: Definition
Def.: A dependence graph is a directed graph G=(V,E) in which E  V  V is a relation.
If (v1, v2)  E, then v1 is called an immediate predecessor of v2 and v2 is called an immediate successor of v1.
Suppose E* is the transitive closure of E. If (v1, v2)  E*, then v1 is called a predecessor of v2 and v2 is called a successor of v1.
Nodes could be programs or simple operations
Sequence constraint

## Slide 15: Dependence graph: Timing information
Dependence graphs may contain additional information, for example:
  Timing information
Arrival time
deadline

## Slide 16: Dependence graph: I/O-information

## Slide 17: Dependence graph: Shared resources

## Slide 18: Dependence graph: Periodic schedules
  A job is single execution of the dependence graph
  Periodic dependence graphs are infinite

## Slide 19: Dependence graph: Hierarchical task graphs

## Slide 20: Communication
  Shared memory
memory
Comp-1
Comp-2
Variables accessible to several components/tasks.
Model mostly restricted to local systems.

## Slide 21: Shared memory
thread a { u = 1; .. P(S) //obtain mutex
if u<5 {u = u + 1; ..} // critical section V(S) //release mutex }
thread b { .. P(S) //obtain mutex
u = 5 // critical section V(S) //release mutex }
  Unexpected u=6 possible if P(S) and V(S) is not used (double context switch before execution of {u = u+1}
  S: semaphore
  P(S) grants up to n concurrent accesses to resource
  n=1 in this case (mutex/lock)
  V(S) increases number of allowed accesses to resource
  Thread-based (imperative) model should be supported by mutual exclusion for critical sections

## Slide 22: On-Site Exercise
thread a { u = 3; //op a1 P(s);
if u<10 //op a2 {u = u + 1; ..} //op a3 else u=5; //op a4 V(s);
}
thread b { u = 2; //op b1
P(s);
if u<4 //op b2 {u = u + 4; ..} //op b3 else u=10; //op b4 V(s);
}
Each thread is supposed to be executed once.
Threads can be executed in any sequence and the execution can switch between the two threads at any time.
For the sake of simplicity, we assume that each operation is executed in an atomic manner, i.e. there is no switch (called context switch) during the execution of ax and thread by.
Which values of u are possible at the completion of both tasks?

## Slide 23: Non-blocking/asynchronous message passing
Sender does not have to wait until message has arrived;
…
send ()
…
…
receive ()
…
Potential problem: buffer overflow

## Slide 24: Blocking/synchronous message passing - rendez-vous
Sender will wait until receiver has received message
…
send ()
…
…
receive ()
…
No buffer overflow, but reduced performance.

## Slide 25: Organization of computations within the components (1)
  Finite state machines

## Slide 26: Organization of computations within the components (2)
  Discrete event model
a
b
c
time
action
a:=5 b:=7 c:=8 a:=6 a:=9
queue
5 10 13 15 19
5
7
8
6
  Von Neumann model
Sequential execution, program memory etc.

## Slide 27: Organization of computations within the components (3)
  Differential equations
  Data flow (models the flow of data in a distributed system)
  Petri nets (models synchronization in a distributed system)

## Slide 28: Summary
Requirements for specification & modeling
  Hierarchy
  ..
  Appropriate model of computation
Models of computation =
    Dependence graphs
    models for communication
    models of components