## Slide 1: Modules + Processes
P. Marwedel*
Informatik 12, U. Dortmund
* Partially using slides prepared by Tatjana Stankovic from the University of Nis (Serbia and Montenegro), visiting the University of Dortmund under the TEMPUS program.
These slides contain Microsoft cliparts. All usage restrictions apply.

## Slide 2: Contents
  Introduction
  Data types
  A Notion of Time
  Modules
  Concurrency
  Structure
  Communication, Channels
  Ports & Interfaces
  Advanced Topics

## Slide 3: SystemC language architecture
C++ Language Standard
Core Language
Modules
Ports
Processes
Events
Interfaces
Channels
Event-driven simulation kernel
Data types
Bits and bit-vectors
Arbitrary precision integers
Fixed-point numbers
4-valued logic types, logic-vectors
C++ user defined types
Elementary Channels
Signal, Timer, Mutex, Semaphore, FIFO, etc
Channels for MoCs
Kahn process networks, SDF, etc
Methodology-specific Channels
Master/Slave library

## Slide 4: Modules
  Modules are basic building blocks of a SystemC design
  A module contains
    processes (→ functionality)
    and/or sub-modules (→ hierarchical structure)
  Modules can be
    described with the SC_MODULE macro
    or derived explicitly from sc_module

## Slide 5: Modules
SC_MODULE is a macro shorthand for deriving module classes from the library class sc_module.
Syntax:
SC_MODULE (module_name) { module_body
};
Definition of SC_MODULE: #define SC_MODULE (module_name) \ struct module_name: public sc_module

## Slide 6: Elements of the module body
SC_MODULE( module_name ) {
// Declaration of module ports
// Member channel instances
// Member data instances
// Member module instances (sub-designs)
// Constructor
// Destructor
// Process member functions (processes)
// Helper functions
};

## Slide 7: The SC_MODULE Class Constructor: SC_CTOR
The constructor must
  Initialize/allocate sub-designs
  Connect sub-designs
  Declare event sensitivities
  Register processes with the SystemC kernel.
Syntax for SC_CTOR: SC_CTOR(module_name)
: Initialization // optional
{ sub-design allocation
sub-design connectivity
process_registration
miscellaneous setup
}
A module must contain a C++ constructor. Constructors should be built using the SystemC macro SC_CTOR or include SC_HAS_PROCESS (module_name);

## Slide 8: Contents
  Introduction
  Data types
  A Notion of Time
  Modules
  Concurrency
  Structure
  Communication, Channels
  Ports & Interfaces
  Advanced Topics

## Slide 9: Processes
Definition: A SystemC process is a member function or class method of an SC_MODULE that is invoked by the scheduler of the SystemC simulation kernel.
Syntax:
void process_name(void);

## Slide 10: SC_THREAD
Threads are simple processes created with the SC_THREAD macro.
Syntax: SC_THREAD(process_name);
Registration by using the macro within the constructor.
Context:
SC_MODULE(simple_process){
SC_CTOR(simple_process) {
SC_THREAD(thread_process); } void thread_process(void); };

## Slide 11: SC_THREAD
Processes created using SC_THREAD
  are started once,
  execute until they call wait() or return, (wait() may be called indirectly via blocking read or write calls)
  frequently comprise infinite loops including wait calls,
  provide persistence for all local variables,
  roughly correspond to processes in an operating system using "cooperative multitasking“ or coroutines.

## Slide 12: SC_THREAD::wait()
Examples: wait(time);
wait(event);
wait(event [, | event]); // any event causes resume
wait(event [, & event]); // all events req. for resume
wait(timeout, event); // event with timeout
wait(); // use static sensivity
Function time_out() may be called immediately after a wait to check if wait was terminated by timeout.

## Slide 13: SC_METHOD
Macro SC_METHOD can be used to create a process within a constructor. Such a process
  Always runs to completion;
  Cannot call wait() or blocking read and write methods.
  Is more efficient than processes created with SC_THREAD.
  Looses the values of all variables upon exit.

## Slide 14: next_trigger()
The next_trigger() method can be used to specify the sensivity of SC_METHODs. The last call of next_trigger preceding an exit from an SC_METHODs specifies the condition for re-entry.
Example: next_trigger(time);
next_trigger(event [, | event]); // any event causes restart
next_trigger(event [, & event]); // all events req. for restart
next_trigger(timeout, event); // event with timeout
next_trigger(); // back to static sensivity

## Slide 15: Static sensivity
Static sensivity is an alternative to using wait() or next_ trigger(). Static sensivity is established at compile time.
Static sensivity applies to the most recent process registration.
2 syntactical forms:
  Streaming style: sensitive << event [ <<event ] …;
  "Functional style" sensitive (event [, event] ..);

## Slide 16: don't_initialize
Normally, all processes are started initially.
This can be avoided by calling dont_initialize().
The call must follow process registration.
A static sensivity list should be used with dont_initialize, otherwise the process would never be executed.
Example: … SC_METHOD(attendant_method); sensitive(fillup_request); dont_initialize(); …

## Slide 17: Contents
  Introduction
  Data types
  A Notion of Time
  Modules
  Concurrency
  Structure
  Communication, Channels
  Ports & Interfaces
  Advanced Topics

## Slide 18: Design Hierarchy
Example
sc_main
car_i
eng_i
body_i
fuelmix_i
exhaust_i
cyl_i1
wheel_FR
wheel_FL
cyl_i2
Different module instantiation approaches:
  in the header or the implementation file,
  direct instantiation in declaration or dynamic creation with pointers,
  at top level of the hierarchy or at some other level.
Combinations thereof.

## Slide 19: Direct Top-Level Instantiation
Example: //file: main.cpp
#include "Wheel.h"
int sc_main (int argc, char* argv[] {
Wheel wheel_FL("wheel_FL");
Wheel wheel_FR("wheel_FR");
sc_start();
}
Simple and to the point.

## Slide 20: Indirect Top-Level Instantiation
Example: //file: main.cpp
#include "Wheel.h"
int sc_main (int argc, char* argv[] {
Wheel* wheel_FL; // pointer to FL wheel
Wheel* wheel_FR; // pointer to FR wheel
wheel_FL = new Wheel("wheel_FL"); //create FL
wheel_FR = new Wheel("wheel_FR"); //create FR
sc_start();
delete wheel_FL;
delete wheel_FR;
}
More code, but more flexible: looping, arrays, if then etc. possible.

## Slide 21: Direct Sub-Module Header-Only Instantiation
Example: //file: Body.h
#include "Wheel.h"
SC_MODULE(Body) {
Wheel wheel_FL;
Wheel wheel_FR;
SC_CTOR(Body) : wheel_FL("wheel_FL"), //initialization wheel_FR("wheel_FR") //initialization
{
// other initialization
}
}
Initializer list to be used due to C++ rules

## Slide 22: Indirect Sub-Module Header-Only Instantiation
Example: //file: Body.h
#include "Wheel.h"
SC_MODULE(Body) {
Wheel* wheel_FL;
Wheel* wheel_FR;
SC_CTOR(Body) { wheel_FL = new Wheel("wheel_FL"); wheel_FR = new Wheel("wheel_FR");
// other initialization
}
};
Easier to read than direct method.

## Slide 23: Direct Sub-Module Instantiation
//file: Body.h
#include "Wheel.h"
SC_MODULE(Body) {
Wheel wheel_FL;
Wheel wheel_FR;
SC_HAS_PROCESS(Body);
Body(sc_module_name nm);
};
//file: Body.cpp
#include "Body.h" // Constructor:
Body::Body(sc_module_name nm)
: wheel_FL("wheel_FL"),
wheel_FR("wheel_FR"),
sc_module(nm)
{ .. other initialization ..}
Moves the complexity of initialization to the implementation, hides it from the users of the header file.

## Slide 24: Indirect Sub-Module Instantiation
//file: Body.h
struct Wheel;
SC_MODULE(Body) {
Wheel* wheel_FL;
Wheel* wheel_FL;
SC_HAS_PROCESS(Body);
Body(sc_module_name nm);
};
//file: Body.cpp
#include "Wheel.h" // Constructor:
Body::Body(sc_module_name nm)
: sc_module(nm)
{wheel_FL=new Wheel("wheel_FL");
wheel_FR=new Wheel("wheel_FR");
.. other initialization .. }
Moves the complexity of initialization to the implementation, hides it from the users of the header file.

## Slide 25: Contrasting Implementation Approaches
Hides sub-module headers and implementation, dynamically configurable
Indirect
with separate compilation
Module
Requires sub-module headers
Hides implementation
Direct with separate compilation
Module
Involves pointers
All in one file, dynamically configurable
Indirect
Header only
Module
Requires sub-module headers
All in one file, easier to understand
Direct
Header only
Module
Involves pointers
Dynamically configurable
Indirect
Main
Inconsistent with other levels
Least code
Direct
Main
Cons
Pros
Allocation
Level

## Slide 26: Hello World in SystemC
#ifndef HELLO_SYSTEMC_H
#define HELLO_SYSTEMC_H
//FILE:Hello_SystemC.h
#include <systemc.h>
#include <iostream>
SC_MODULE(Hello_SystemC) {
sc_in_clk clk_pi;
void Hello_SystemC::main_method(void);
SC_CTOR(Hello_SystemC) {
SC_METHOD(main_method);
sensitive << clk_pi.neg();
dont_initialize();
} };
#endif
//FILE:main.cpp
#include <Hello_SystemC.h>
int sc_main(int argc, char* argv[]) {
const sc_time t_PERIOD(8,SC_NS);
sc_clock clk("clk",t_PERIOD);
Hello_SystemC iHello_SystemC ("iHello_SystemC");
iHello_SystemC.clk_pi(clk);
sc_start(10);
return 0; }
//FILE:Hello_SystemC.cpp
#include <Hello_SystemC.h>
void Hello_SystemC::main_method(void) {std::cout << sc_time_stamp() << " Hello world!" << std::endl;
}
Source & ©: D. Black, J. Donovan, http://eklectically.com/Book/; All usage restrictions imposed by the authors apply.
Notes: Ginge auch einfacher, wenn man nicht die Benutzung eines Hardware-Bausteins beschreiben wollte.
1. Beschreibung der Implementierung von sc_main

## Slide 27: SystemC language architecture
C++ Language Standard
Core Language
Module
Ports
Processes
Events
Interfaces
Channels
Event-driven simulation kernel
Data types
Bits and bit-vectors
Arbitrary precision integers
Fixed-point numbers
4-valued logic types, logic-vectors
C++ user defined types
Elementary Channels
Signal, Timer, Mutex, Semaphore, FIFO, etc
Channels for MoCs
Kahn process networks, SDF, etc
Methodology-specific Channels
Master/Slave library

## Slide 28: Contents
  Introduction
  Data types
  A Notion of Time
  Modules
  Concurrency
  Structure
  Communication
  Channels
  Advanced Topics

## Slide 29: Events
An event is an object represented by sc_events, that determines whether and when a process‘s execution should be triggered or resumed.
An event is used to represent a condition that may occur during the course of simulation and to control the triggering of processes accordingly.
The sc_event class provides basic synchronization for processes.

## Slide 30: Events
Distinction between
  event (“subjunctive mood‘‘) and
  actual occurrence of an event (‘‘indicative mood‘‘).
An event is usually associated with some change of state in a process or of a channel.
The owner of the event is responsible for reporting the change to the event object.
The act of reporting the change to the event is called notification.

## Slide 31: Event
Event notification and process triggering
channel

## Slide 32: Triggering events: .notify
Events are created with .notify().
  Immediate notify's move waiting processes immediately from the waiting pool to the ready pool. Examples: event_name.notify(); notify(event_name);
  Delayed notification: event_name.notify(SC_ZERO_TIME); notify(event_name, SC_ZERO_TIME); Processes waiting will execute at the next  cycle.
  Timed notification lets processes execute after the indicated time. event_name.notify(t); notify(event_name, t);

## Slide 33: Simulation engine (simplified)
sc_main:
SystemC simulation kernel:
simulation
sc_start():
initialize
cleanup
elaborate
Elaboration: simulation parameters established
Initialization: threads started (placed in ready pool)
all threads exited  simulation time is over

## Slide 34: Transitions between thread states - Predicate/transition net model  activity chart  queuing model -
run


ready ={}
capacity=1
wait(t)
ready
@ simulation start:
dont_inits: placed in  waiting for static sensivity event
others: placed in ready
notify(event)*
notify(event, SC_ZERO_TIME)*
wait (event)
timeout°/advance
simulation time
*for (ready={}={}): for threads waiting for event
°timeout=(ready={}={})thread waiting time = min. of all waiting times
wait(SC_ZERO_TIME)
next_trigger  notify, except that methods are called again
static sensivity  wait for fixed event
return
diagram not found elsewhere
update signals each time ready becomes {} (end of  cycle), see sc_signal
prio=1
prio=1
prio=2
prio=3
prio=4
prio=4

## Slide 35: Transitions between thread states - Predicate/transition net model  activity chart  queuing model -
run


ready ={}
capacity=1
wait(t)
ready
@ simulation start:
dont_inits: placed in  waiting for static sensivity event
others: placed in ready
notify(event)*
notify(event, SC_ZERO_TIME)*
wait (event)
timeout°/advance
simulation time
wait(SC_ZERO_TIME)
non-deterministic choice between ready threads

## Slide 36: Transitions between thread states - Predicate/transition net model  activity chart  queuing model -
run


ready ={}
capacity=1
wait(t)
ready
@ simulation start:
dont_inits: placed in  waiting for static sensivity event
others: placed in ready
notify(event)*
notify(event, SC_ZERO_TIME)*
wait (event)
timeout°/advance
simulation time
wait(SC_ZERO_TIME)
ready pool emptied, before next  cycle starts

## Slide 37: Transitions between thread states - Predicate/transition net model  activity chart  queuing model -
run


ready ={}
capacity=1
wait(t)
ready
@ simulation start:
dont_inits: placed in  waiting for static sensivity event
others: placed in ready
notify(event)*
notify(event, SC_ZERO_TIME)*
wait (event)
timeout°/advance
simulation time
wait(SC_ZERO_TIME)
next  cycle

## Slide 38: Transitions between thread states - Predicate/transition net model  activity chart  queuing model -
run


ready ={}
capacity=1
wait(t)
ready
@ simulation start:
dont_inits: placed in  waiting for static sensivity event
others: placed in ready
notify(event)*
notify(event, SC_ZERO_TIME)*
wait (event)
timeout°/advance
simulation time
wait(SC_ZERO_TIME)
next  cycle …

## Slide 39: Transitions between thread states - Predicate/transition net model  activity chart  queuing model -
run


ready ={}
capacity=1
wait(t)
ready
@ simulation start:
dont_inits: placed in  waiting for static sensivity event
others: placed in ready
notify(event)*
notify(event, SC_ZERO_TIME)*
wait (event)
timeout°/advance
simulation time
wait(SC_ZERO_TIME)
there can be several  cycles

## Slide 40: Transitions between thread states - Predicate/transition net model  activity chart  queuing model -
run


ready ={}
capacity=1
wait(t)
ready
@ simulation start:
dont_inits: placed in  waiting for static sensivity event
others: placed in ready
notify(event)*
notify(event, SC_ZERO_TIME)*
wait (event)
timeout°/advance
simulation time
wait(SC_ZERO_TIME)
there can be several  cycles …

## Slide 41: Transitions between thread states - Predicate/transition net model  activity chart  queuing model -
run


ready ={}
capacity=1
wait(t)
ready
@ simulation start:
dont_inits: placed in  waiting for static sensivity event
others: placed in ready
notify(event)*
notify(event, SC_ZERO_TIME)*
wait (event)
timeout°/advance
simulation time
wait(SC_ZERO_TIME)
now the blue thread is the 1st thread to become ready; simulation time is advanced.

## Slide 42: Transitions between thread states - Predicate/transition net model  activity chart  queuing model -
run


ready ={}
capacity=1
wait(t)
ready
@ simulation start:
dont_inits: placed in  waiting for static sensivity event
others: placed in ready
notify(event)*
notify(event, SC_ZERO_TIME)*
wait (event)
timeout°/advance
simulation time
wait(SC_ZERO_TIME)
and the blue thread is executed

## Slide 43: Control flow representation
While there is a process in the  pool
While there is a process in the “”pool
  While there is a process in the ready pool
    {take any process
    execute: evaluate signal changes;
    may send event notifications
      immediate ( put into ready pool),
      delayed ( “” pool, with 0 time)
      timed ( waiting pool, with time)
    until process completes (via return) or suspends (via calls to wait()); process to pool}
  Update pending signal changes; (see sc_signal)
  processes waiting in “” pool  ready pool;
If  process   pool: advance time
// macroscopic time loop
//  time loop
// same  time
ready
run



## Slide 44: Event
Events can have only one pending notification, and retain no „memory“ of past notifications.
Multiple notifications to the same event, without an intermediate trigger are resolved according to the following rule:
An earlier notification will always override one scheduled to occur later, and an immediate notification is always earlier than any -cycle delayed or timed notification.

## Slide 45: sc_event_queue
Event queues allow single events to be scheduled multiple times. If events are scheduled for the same time, they will be separated by a cycle. All scheduled events can be cancelled with the .cancel_all() method.
Example: sc_event_queue action;
action.notify(20,SC_MS); // schedule for 20 ms from now
action.notify(1.5,SC_NS); // schedule for 1.5 ns from now action.notify(SC_ZERO_TIME); // for next  cycle
action.cancel_all();

## Slide 46: Summary
  Modules are key design entities and can be created with SC_MODULE.
  Constructor SC_CTOR or SC_HAS_PROCESS required.
  There are two types of processes within modules:
    SC_THREAD: started once, may contain wait,
    SC_METHOD: run to completion, cannot call wait, may call next_trigger.
  6 different ways of describing structural hierarchy
  Events can be used for notifications
  The simulation cycle uses an evaluation/update cycle for signal updates, corresponding to the -cycle of VHDL.