## Slide 1: Communication
P. Marwedel*
* Partially using slides prepared by Tatjana Stankovic from the University of Nis (Serbia and Montenegro), visiting the University of Dortmund under the TEMPUS program.
These slides contain Microsoft cliparts. All usage restrictions apply.

## Slide 2: Gas station example (1)
Customer 1
Customer 2
Filled!
Fill'er up!

## Slide 3: Gas station example (2)
//BEGIN main.cpp
//See gas_station.h for more information
#include <systemc.h>
#include "gas_station.h"
unsigned errors = 0;
char* simulation_name = "gas_station";
int sc_main(int argc, char* argv[]) {
sc_set_time_resolution(1,SC_NS);
sc_set_default_time_unit(1,SC_NS);
gas_station Charlies("Charlies",/*full1*/10,/*full2*/12,/*filltime*/1.5,/*maxfills*/10);
cout << "INFO: Starting gas_station simulation" << endl;
sc_start();
cout << "INFO: Exiting gas_station simulation" << endl;
cout << "INFO: Simulation " << simulation_name
<< " " << (errors?"FAILED":"PASSED")
<< " with " << errors << " errors"
<< endl;
return errors?1:0;}
Source & ©: D. Black, J. Donovan, http://eklectically.com/Book/; All usage restrictions imposed by the authors apply.

## Slide 4
#ifndef GAS_STATION_H ..
#include <iostream>
using std::cout; using std::endl;
#include <string>
#include <systemc.h>
SC_MODULE(gas_station) { // Local module data
const sc_time t_MIN; bool m_filling; // state of attendant
double m_full1, m_full2; double m_filltime; sc_event e_request1, e_request2;
double m_tank1, m_tank2; unsigned m_count1, m_count2, m_maxcount;
sc_event e_filled; // Constructor
SC_HAS_PROCESS(gas_station);
gas_station( sc_module_name _name,
double full1=10.0, double full2=11.1, double filltime=1.8, unsigned maxcount=5 ) :
sc_module(_name), m_full1(full1), m_full2(full2), m_filltime(filltime), m_tank1(full1),
m_tank2(full1), m_count1(0), m_count2(0), m_maxcount(maxcount), m_filling(false),
t_MIN(1,SC_NS) // treat 1 minute = 1 nanosecond
{ cout << "INFO: Gas station named \"" << name() << "\"" << endl;
cout << "INFO: Customer1 has " << m_full1 << " gallon tank." << endl;
cout << "INFO: Customer2 has " << m_full2 << " gallon tank." << endl;
cout << "INFO: Attendant takes " << m_filltime << " minutes per gallon." << endl;
cout << "INFO: Maximum of " << m_maxcount << " fills per customer." << endl;
SC_THREAD(customer1_thread); sensitive(e_filled);
SC_THREAD(customer2_thread);
SC_METHOD(attendant_method); sensitive << e_request1 << e_request2; dont_initialize();
}//endconstructor gas_station // Declare processes
void customer1_thread(void); void customer2_thread(void); void attendant_method(void);
std::string hms(void); }; // Helper methods
#endif
Source & ©: D. Black, J. Donovan, http://eklectically.com/Book/; All usage restrictions imposed by the authors apply.

## Slide 5: Gas station example (4)
void gas_station::customer2_thread(void) {
for (;;) { // Simulate emptying time
wait((m_full2+rand()%
int(m_full2*0.10))*t_MIN);
cout << "INFO: " << name() << " Customer2 needs gas (1) at " << hms() << endl;
m_tank2 = 0;
do { e_request2.notify(); // fillup! (2)
wait(e_filled); // dynamic sensitivity
} while (m_tank2 == 0);
}//endforever
}//end customer2_thread()
//BEGIN gas_station.cpp (systemc)
#include "gas_station.h"
using std::cout;
using std::endl;
extern unsigned errors;
void gas_station::customer1_thread(void) {
for (;;) { // Simulate gas tank emptying time
wait((m_full1+rand()%int(m_full1*0.10))*t_MIN);
// Force 25% of all fill ups to be simultaneous // with other customers to check contention
if (rand()%4==1) wait(e_request2);
cout << "INFO: " << name() << " Customer1 req. gas (1) at " << hms() << endl;
m_tank1 = 0;
// Request fill up and then wait for acknowledge
do { e_request1.notify(); // I need fill up! (2)
wait(); // static sensitivity Somebody got filled
} while (m_tank1 == 0); // Was it us? yes
}//end forever
}//end customer1_thread()
Source & ©: D. Black, J. Donovan, http://eklectically.com/Book/; All usage restrictions imposed by the authors apply.

## Slide 6: Gas station example (5)
void gas_station::attendant_method(void) {
// ASSERTION: We got here due to either (A) a request in progress
// (B) an event request from a new customer. Since this is an SC_METHOD,
// we maintain a small amount of state, m_filling. Initially, we're not filling.
// Once we get a fillup request, we choose who, initiate filling, and then
// use dynamic sensitivity to delay by the amount of time it takes to fill the
// indicated gas tank.
if (!m_filling) {
// Check customer 1 first (preferential selection)
if (m_tank1 == 0 && m_count1 < m_maxcount) {
cout << "INFO: " << name()
<< " Filling tank1 (3) at "
<< hms() << endl;
next_trigger(m_filltime*m_full1*t_MIN);
m_filling = true;
// Check customer 2 only if no customer 1
} else if (m_tank2 == 0 && m_count2 < m_maxcount) {
cout << "INFO: " << name()
<< " Filling tank2 (3) at "
<< hms() << endl;
next_trigger(m_filltime*m_full2*t_MIN);
m_filling = true;
}//endif
} else {
Source & ©: D. Black, J. Donovan, http://eklectically.com/Book/; All usage restrictions imposed by the authors apply.

## Slide 7: Gas station example (5)
} else {
// We reach here by timing out on filling the tank, so first update
// the tank, counts and issue messages about this event for the
// appropriate customer. Then notify everyone of the event (4)
if (m_tank1 == 0 && m_count1 < m_maxcount) {
m_tank1 = m_full1; m_count1++;
cout << "INFO: " << name() << " Filled tank1 (4) at " << hms() << endl;
} else if (m_tank2 == 0 && m_count2 < m_maxcount) {
m_tank2 = m_full2;
m_count2++;
cout << "INFO: " << name() << " Filled tank2 (4) at " << hms() << endl;
}//endif
e_filled.notify(SC_ZERO_TIME); // We finished filling (4) & are available!
m_filling = false; // go back to waiting
// See if we need to stop the simulation
if (m_count1 == m_maxcount && m_count2 == m_maxcount) {
cout << "WARN: " << name()
<< " No more fuel at "
<< hms() << endl;
sc_stop();
}//endif
}//endif
}//end attendant_method()
Source & ©: D. Black, J. Donovan, http://eklectically.com/Book/; All usage restrictions imposed by the authors apply.

## Slide 8: Gas station example (7)
#include <sstream>
std::string gas_station::hms(void) {
std::ostringstream now;
double mins(sc_simulation_time());
unsigned days = int(mins/(24*60));
mins -= days*24.0*60.0;
unsigned hrs = int(mins/60);
mins -= hrs*60.0;
if (days) now << days << " days ";
if (days||hrs) now << hrs << " hrs ";
now << mins << " mins";
return now.str();
}//end hms()
Source & ©: D. Black, J. Donovan, http://eklectically.com/Book/; All usage restrictions imposed by the authors apply.

## Slide 9: Limitations of gas station model
  Complicated way of finding out, which customer has been served. e.g.: what to do after wait (e_request1 | e_request2)
  Events cannot be used to distribute information
  No mechanism available for accessing shared resources
  Channels
    Primitive channels Inherited from base class sc_prim_channel, include sc_mutex, sc_semaphore, and sc_fifo.
    Hierarchical channels

## Slide 10: Contents
  Introduction
  Data types
  A Notion of Time
  Modules
  Concurrency
  Structure
  Communication, Channels
  Ports & Interfaces
  Advanced Topics

## Slide 11: SystemC language architecture
C++ Language Standard
Core Language
Module
Ports
Processes
Events
Interfaces
Channels
Event-driven simulation kernel
Data types
Bits and bit-vectors
Arbitrary precision integers
Fixed-point numbers
4-valued logic types, logic-vectors
C++ user defined types
Elementary Channels
Signal, Timer, Mutex, Semaphore, FIFO, etc
Channels for MoCs
Kahn process networks, SDF, etc
Methodology-specific Channels
Master/Slave library

## Slide 12: Mutual exclusion: sc_mutex
Global resources can be protected with mutexes.
Mutex associated with resource to be protected.
SystemC provides mutex methods for sc_mutex channels.
Syntax:
sc_mutex name; // declare mutex
name.lock(); // blocking: waiting until mutex is unlocked
name.trylock() // nonblocking: true if success, else false
name.unlock() // free locked mutex
No signal generated if resource is freed (wakeup??)
SC_METHOD cannot use .lock(), since it is blocking.

## Slide 13: sc_mutex: Examples
sc_mutex drivers_seat; …
car->drivers_seat.lock(); // lock seat
car->start(); …
car->stop();
car->drivers_seat.unlock(); // unlock seat
class bus {
sc_mutex bus_access;
void write(int addr, int data) {
bus_access.lock();
// perform write
bus_access.unlock();
} … }; //endclass

## Slide 14: Semaphores
Sometimes,  1 copies of global resources are available.
Can be modeled with class sc_semaphore.
Number of copies is part of the declaration.
Syntax:
sc_semaphore name(count); // declare semaphore
name.wait(); // blocking: waiting until available
name.trywait() // nonblocking: true if success
name.get_value() // return number from semaphore
name.post() // free semaphore
SC_METHOD cannot use .wait(), since it is blocking.
Notes: Trywait: Exploiting cooperative multitasking: no preemption between the 2 lines!

## Slide 15: sc_semaphore: Examples (1)
Example: Gas station with 12 pumps
SC_MODULE (gas_station) {
sc_semaphore pump(12); // 12 pumps
void customer1_thread {
for (;;) { // wait till tank empty
… // find an available gas pump:
pump.wait();
// fill and pay
pump.post();
}};

## Slide 16: Modeling a multiport memory
class multiport_RAM {
sc_semaphore read_ports(3);
sc_semaphore write_ports(2);
..
void read(int addr, int& data) {
read_ports.wait();
//perform read
read_ports.post();
}
void write(int addr, int data) {
write_ports.wait();
//perform write
write_ports.post();
}…};//endclass

## Slide 17: Communication by FIFOs
In the early design stages, STL’s unbounded deque (double ended queue) may be sufficient.
More details available with sc_fifo<>.
Default depth: 16;
Data type needs to be specified.
Syntax & methods: sc_fifo<element_typename> name(size);
name.write(value);
name.read(reference);
…= name.read(); // function style
Potentially blocking reads and writes.

## Slide 18: Communication by FIFOs (2)
Syntax & methods (cont’ed):
  if (name.num_available()==0) wait(name.data_written_event()); Allows test before waiting for next element to be read.
  if (name.num_free()==0) next_trigger(name.data_read_event()); Allows test before waiting for next element to be written.
Notes: Exploiting cooperative multitasking: no preemption between the 2 lines!

## Slide 19: Kahn process networks
Better performance if storing pointers, not structures;
shared_ptr<> from GNU Boost library recommended.
Assuming finite length is no problem:
SC_MODULE(kahn_ex) { …
sc_fifo<double> a, b, y; …
// Constructor
kahn_ex::kahn_ex(): a(19), b(10), y(20) {…}
void kahn_ex::addsub_thread() {
for (;;) {
y.write(kA*a.read() + kB*b.read());
y.write(kA*a.read() - kB*b.read());
} //end forever
}

## Slide 20: Deterministic models of synchronous hardware
sc_signal (and sc_buffer) correspond to signals in VHDL:
they use the evaluation-update paradigm:
  Every channel has 2 storage locations:
    current value and
    new value.
  Writes are updating new value,
  Reads are reading current value
  request_update(): called by write(), causes kernel to call update() during the update phase, for each channel that requested an update
  update() copies new value to current value, but may also resolve contention or notify events.
Evaluate-update cycle enables deterministic communication.

## Slide 21: sc_signal
Syntax:
  sc_signal <datatype> signame [,signame] ..;
  signame.write(newvalue) write includes evaluate phase of behavior + call to protected sc_prim_channel::request_update(); Call to sc_signal::update() is hidden, occurs in update phase due to request_update; Within each –cycle, only a single process can write to channels of type sc_signal, last value being retained.
  signame.read(varname)

## Slide 22: sc_signal: Example
int c;
sc_signal<sc_string> sig;
// initialization during 1st delta cycle
sig.write("Hello");
c=1;
cout << "c: " << c << " "
<< "sig:" << sig << endl;
Wait(SC_ZERO_TIME);
// 2nd delta cycle
c=2;
sig.write("World");
cout << "c: " << c << " "
<< "sig:" << sig << endl;
wait(SC_ZERO_TIME);
// 3rd delta cycle …
Output:
c: 1 sig: ' '
c: 2 sig: 'Hello'
Recommended suffix _sig for signals to indicate delayed update.

## Slide 23: Control flow representation
While there is a process in the  pool
While there is a process in the “”pool
  While there is a process in the ready pool
    {take any process
    execute: evaluate signal changes;
    may send event notifications
      immediate ( put into ready pool),
      delayed ( “” pool, with 0 time)
      timed ( waiting pool, with time)
    until process completes (via return) or suspends (via calls to wait()); process to pool}
  Update pending signal changes;
  processes waiting in “” pool  ready pool;
If  process   pool: advance time
// macroscopic time loop
//  time loop
// same  time
ready
run



## Slide 24: Transitions between thread states - Predicate/transition net model  activity chart  queuing model -
run


ready ={}
capacity=1
wait(t)
ready
@ simulation start:
dont_inits: placed in  waiting for static sensivity event
others: placed in ready
notify(event)
notify(event, SC_ZERO_TIME)
wait (event)
timeout/advance
simulation time
wait(SC_ZERO_TIME)
return
diagram not found elsewhere
update signals each time ready becomes {} (end of  cycle)
prio=1
prio=1
prio=2
prio=3
prio=4
prio=4

## Slide 25: Dangerous overloading of =
varname = signame.read();
signame = newvalue;
varname = signame;
are also legal, but dangerous, since they hide the evaluate-update cycle.

## Slide 26: Multiple writes in a -cycle
Syntax:
sc_signal_resolved name;
sc_signal_rv<width> name; //*
Semantics same as for sc_signal<sc_logic>, except that multiple writes are permitted in a -cycle. Resolution is predefined as follows:
'Z'
'X'
'1'
'0'
'Z'
'X'
'X'
'X'
'X'
'X'
'1'
'X'
'1'
'X'
'1'
'0'
'X'
'X'
'0'
'0'
'Z'
'X'
'1'
'0'
A\B
bus
tristate
Z
1
0
X
* rv means: resolved vector
Changing the resolution function is a little awkward (see Black & Donovan)

## Slide 27: Template specializations of sc_signal<bool> and sc_signal<sc_logic>
Signals of specializations sc_signal<bool> and sc_signal<sc_logic> support the following extensions:
Syntax: sensitive << signame.posedge_event()
<< signame.negedge_event();
wait(signame.posedge_event() | signame.negedge_event());
if (signame.posedge_event() | signame.negedge_event()) {…
Semantics: posedge is any transition to '1', negedge is any transition to '0'.

## Slide 28: SystemC language architecture
C++ Language Standard
Core Language
Module
Ports
Processes
Events
Interfaces
Channels
Event-driven simulation kernel
Data types
Bits and bit-vectors
Arbitrary precision integers
Fixed-point numbers
4-valued logic types, logic-vectors
C++ user defined types
Elementary Channels
Signal, Timer, Mutex, Semaphore, FIFO, etc
Channels for MoCs
Kahn process networks, SDF, etc
Methodology-specific Channels
Master/Slave library

## Slide 29: Ports
How to communicate between local modules?
  Implicit interfaces such a global variables should be avoided
  Ports provide the well-defined boundaries through which modules interact
  Ports are connected to channels via interfaces. These provide the required encapsulation.
  Ports are “kind of” pointers to channels.

## Slide 30: Initial example
“A_thread in module modA communicates a value contained in local variable v by calling the write method of the parent module’s channel c.”
A_thread does not need to use anything but the write method.
Separation of concerns enabled by  interfaces.
write().. read()
A_thread
B_thread
sc_fifo<int> c;
modA mA
modB mB
port pA
port pB
pA->write(v);
W=pB->read();

## Slide 31: Using virtual methods and polymorphism in C++
struct multiport_memory_arch: public my_interface { virtual void write(unsigned addr, int data) { mem[addr] = data; } // end write virtual int read(unsigned addr) ) { return mem[addr]; } // end read private: int mem[1024];
};
struct multiport_memory_RTL: public my_interface { virtual void write(unsigned addr, int data) { // complex details of memory write
} // end write virtual int read(unsigned addr) ) { // complex details of memory read
} // end read private: // complex details of memory storage
};
Memories!
Oops! Memories!
2 Memory models

## Slide 32: Application to memory testing
void memtest(my_interface mem) { //complex memory test }
multiport_memory_arch fast;
multiport_memory_RTL slow;
memtest(fast);
memtest(slow);
The same memory test method will use different levels of precision for the memory model.
Memtest
Call graph
write, read
type-dependent
write (RTL)
write (arch)

## Slide 33: Interfaces in C++
Abstract classes = Classes never used directly. Abstract classes usually only contain pure virtual functions. Example:
struct My_interface {
virtual T1 My_methA(…)=0;
virtual T2 My_methB(…)=0;
};
class My_Derived1
: public My_Interface{
T1 My_methA(…) {…}
T2 My_methB(…) {…}
private:
T5 my_data1;
};
class My_Derived2
: public My_Interface{
T1 My_methA(…) {…}
T2 My_methB(…) {…}
private:
T7 my_data4;
};
Classes containing no data members and only pure virtual methods are called interface classes.
Polymorphism: calling My_methA results
  in call to My_Derived1::My_methA if object is of type My_Derived1
  and in call to My_Derived2::My_methA if object is of type My_Derived2

## Slide 34: Definition of interfaces and channels
SystemC interface: abstract class inheriting from sc_interface, providing only pure virtual declarations of methods referenced by SystemC channels and ports.
No implementations or data are provided in an interface.
SystemC channel: class implementing  1interface classes, inheriting from sc_channel or sc_prim_channel.
Channel implements all methods of inherited interface classes.
By using interfaces to connect to channels, we can implement modules independently of the implementation details of the communication channels.

## Slide 35: Power of interfaces
modA
modB
modA
modB
In one design, modules are connected via a FIFO, in a second design with a complex bus. If the interfaces, in this case sc_fifo_out_if<> and sc_fifo_in_if<> remain the same, no change to modA and modB is required if we replace the channel.
Key for re-use of intellectual property (IP).
sc_fifo<T>
sc_fifo_out_if<>
sc_fifo_in_if<>
cpx_bus<T>

## Slide 36: Simple SystemC Port Declarations
Definition: A SystemC port is a class templated with and inheriting from a SystemC interface.
Ports allow access of channels across module boundaries.
Syntax:
sc_port<interface> portname; //used @module class definition
Example:
SC_MODULE(stereo_amp) {
sc_port<sc_fifo_in_if<int> > soundin_p;
sc_port<sc_fifo_out_if<int> > soundin_p;
…};
Do no omit blank!

## Slide 37: Summary
  Gas station example
  Channels
    sc_mutex,
    sc_semaphore
    sc_fifo,
    sc_signal,
    -cycles,
    sc_signal_resolved
  Polymorphism & Interfaces
  Ports (1)