## Slide 1: Ports & Interfaces
P. Marwedel*
Informatik 12, U. Dortmund
* Partially using slides prepared by Tatjana Stankovic from the University of Nis (Serbia and Montenegro), visiting the University of Dortmund under the TEMPUS program.
These slides contain Microsoft cliparts. All usage restrictions apply.

## Slide 2: Contents
  Introduction
  Data types
  A Notion of Time
  Modules
  Concurrency
  Structure
  Communication, Channels
  Ports & Interfaces
  Advanced Topics

## Slide 3: Definition of interfaces and channels
SystemC interface: abstract class inheriting from sc_interface, providing only pure virtual declarations of methods referenced by SystemC channels and ports.
No implementations or data are provided in an interface.
SystemC channel: class implementing  1interface classes, inheriting from sc_channel or sc_prim_channel.
Channel implements all methods of inherited interface classes.
By using interfaces to connect to channels, we can implement modules independently of the implementation details of the communication channels.

## Slide 4: Power of interfaces
modA
modB
modA
modB
In one design, modules are connected via a FIFO, in a second design with a complex bus. If the interfaces, in this case sc_fifo_out_if<> and sc_fifo_in_if<> remain the same, no change to modA and modB is required if we replace the channel.
Key for re-use of intellectual property (IP).
sc_fifo<T>
sc_fifo_out_if<>
sc_fifo_in_if<>
cpx_bus<T>

## Slide 5: Simple SystemC Port Declarations
Definition: A SystemC port is a class templated with and inheriting from a SystemC interface.
Ports allow access of channels across module boundaries.
Syntax:
sc_port<interface> portname; //used @module class definit.
Example:
SC_MODULE(stereo_amp) {
sc_port<sc_fifo_in_if<int> > soundin_p;
sc_port<sc_fifo_out_if<int> > soundout_p;
…};
Do no omit blank!

## Slide 6: Ports
Ports have a mode (direction) and a type
  mode: in, out, inout
  type: C++ type, SystemC type, user-defined type
  Examples:
    sc_in<type> in_port_name; //input port declaration
    sc_out<type> out_port_name; //output port declaration
    sc_inout<type> inout_port_name; //bidirectional port
    sc_out<int> result [32]; //vector port/port array

## Slide 7: Where to put the ports?
Example: SC_MODULE(adder) {
  sc_in<int> a;
  sc_in<int> b;
  sc_out<int> c;
  // processes, etc
  SC_CTOR(adder) {
// body of constructor
// process declaration, sensitivities etc
    c.initialize(0);
  }
};

## Slide 8: Ports
User can derive specialized ports from the sc_port class;
Signal ports are provided by SystemC:
template<class T>
class sc_in : public sc_port<sc_signal_in_if<T> > …;
template<class T>
class sc_inout : public sc_port<sc_signal_inout_if<T> > ..

## Slide 9: Accessing ports from within a process
sc_port overloads the -> operator to allow access to ports.
Example:
void Video_Mixer::Mixer_thread() {
…
switch (control->read()) {
case MOVIE: K.write(0.0f); break;
case MENU: K.write(1.0f); break;
case FADE: K.write(0.5f); break;
default: status->write(Error); break;
}
…
}
Any interface method can be invoked through the port.
read() and write() are interface method calls.

## Slide 10: SystemC language architecture
C++ Language Standard
Core Language
Module
Ports
Processes
Events
Interfaces
Channels
Event-driven simulation kernel
Data types
Bits and bit-vectors
Arbitrary precision integers
Fixed-point numbers
4-valued logic types, logic-vectors
C++ user defined types
Elementary Channels
Signal, Timer, Mutex, Semaphore, FIFO, etc
Channels for MoCs
Kahn process networks, SDF, etc
Methodology-specific Channels
Master/Slave library

## Slide 11: Interfaces
Consist of a set of operations.
Specify only the signature of an operation
  name, parameter, return value
All SystemC interfaces derived from sc_interface
  Contains a virtual function called register_port()
    Connects a port to a channel through the interface
    Arguments: port object and type name of the interface that port accepts

## Slide 12: sc_mutex_if
struct sc_mutex_if: virtual public sc_interface {
virtual int lock() = 0;
virtual int trylock() = 0;
virtual int unlock() = 0;
};
sc_mutex also provides interfaces to be used with ports
No method for event sensivity.

## Slide 13: sc_semaphore_if
struct sc_semaphore_if: virtual public sc_interface {
virtual int wait() = 0;
virtual int trywait() = 0;
virtual int post() = 0;
virtual int get_value() const = 0;
};
sc_semaphore also provides interfaces to be used with ports
Again no method for event sensivity.

## Slide 14: sc_fifo interfaces (1)
Two interfaces are provided for sc_fifo:
  sc_fifo_out_if<>
  sc_fifo_in_if<>
Together, they provide all methods for sc_fifo.

## Slide 15: sc_fifo interfaces (2): sc_fifo_out_if<>
template <class T>
struct sc_fifo_out_if: virtual public sc_interface {
virtual void write(const T&) =0;
virtual bool nb_write(const T&) =0;
virtual int num_free() const =0;
virtual const sc_event& data_read_event() const =0;
…
};

## Slide 16: sc_fifo interfaces (3): sc_fifo_in_if<>
template <class T>
struct sc_fifo_in_if: virtual public sc_interface {
virtual void read( T& ) = 0;
virtual T read() = 0;
virtual bool nb_read( T& ) =0;
virtual int num_available() const =0;
virtual const sc_event& data_written_event() const =0;
…
};

## Slide 17: sc_signal interfaces
E.g.:
  template <class T>
  struct sc_signal_inout_if: virtual public sc_signal_in_if<T> { virtual void write(const T&) =0; … };
  #define sc_signal_out_if sc_signal_inout_if
sc_signal_inout_if provides all methods for the other two interfaces
Interfaces are provided for sc_signal:
  sc_signal_out_if<>
  sc_signal_in_if<>
  sc_signal_inout_if<>
Together, they provide all methods for sc_signal.

## Slide 18: Ports and static sensivity
It is frequently desirable to describe processes which are sensitive to events on ports.
Ports are essentially pointers, which may be undefined until the end of elaboration (IEEE 1666 insists on this).
  Ports are undefined, when static sensitivity clauses are analyzed.
  Connection to events has to be deferred, events have to be located “later”.
  Event finders are methods to be used in static sensivity lists to establish sensitivity to ports.
  In order to avoid the burden of writing event finders, some port specializations provide methods already including event finders.

## Slide 19: sc_in<T>
sc_in is a specialization sc_port<sc_signal_in_if<T> >
Provided methods include event finders:
sc_in<T> name_sig_ip;
sensitive << name_sig_ip.value_changed();
// for T= bool and T= sc_logic:
sc_in<bool> name_bool_sig_ip;
sc_in<sc_logic> name_log_sig_ip;
sensitive << name_log_ip_sig.pos();
sensitive << name_bool_ip_sig.neg();
“.”-notation discouraged but needed in declaration
“->” - notation preferred.

## Slide 20: sc_out<T>
Similarly, sc_out provides methods value_changed() and initialize()

## Slide 21: Example: header
//file LFSR_ex.h
#ifndef LFSR_EX_H
#define LFSR_EX_H
SC_MODULE (LFSR_ex) // ports
sc_in<bool> sample;
sc_out<sc_int<32> > signature;
sc_in<bool> clock;
sc_in<bool> reset;
SC_CTOR(LFSR_ex){
SC_METHOD(LFSR_ex_method);
sensitive << clock.pos() << reset;
signature.initialize(0);
}
void LFSR_ex_method();
sc_int<32> LFSR_reg; };
#endif
sample
…
signature
clock
reset


## Slide 22: Example: Implementation
//file LFSR_ex.cpp
#include <systemc.h>
#include “LFSR_ex.h”
void LFSR_ex::LFSR_ex_method() {
if (reset->read() == true) {
LFSR_reg = 0;
signature->write(LFSR_reg);
} else {
bool lsb = LFSR_reg[31] ^ LFSR_reg[25] ^ LFSR_reg[22]
^ LFSR_reg[21] ^ LFSR_reg[15] ^ LFSR_reg[11] ^ LFSR_reg[10]
^ LFSR_reg[ 9] ^ LFSR_reg[ 7] ^ LFSR_reg[ 6] ^ LFSR_reg[ 4]
^ LFSR_reg[ 3] ^ LFSR_reg[ 1] ^ LFSR_reg[ 0] ^ sample->read();
LFSR_reg.range(31,1) = LFSR_reg.range(30,0); LFSR_reg[0] = lsb;
signature->write(LFSR_reg);
}//endif
}
sample
…
signature
clock
reset


## Slide 23: Standard Graphical Notation
sc_channel
sc_port
sc_interface
sc_event

## Slide 24: Port connection mechanics
Modules are connected to channels after modules and channels have been instantiated.
Syntax:
mod_instance(channel_instance, …); // positional (risky)
mod_inst.portname(channel_instance); // named (safer)

## Slide 25: Example: Video mixer
Video_Mixer
Rgb2YCrCb_i
YCrCb_Mixer_i
dvd_in
video_po
control
rgb_pi
ycrcb_po
a_pi
b_pi
y_po
status
K_pi
K
ycrcb_graphics
rgb_graphics
as (in)complete as in "the source"

## Slide 26: Example: Video mixer (2)
//File: Rgb2YCrCb.h
SC_MODULE(Rgb2YCrCb) {
sc_port<sc_fifo_in_if<RGB_frame> > rgb_pi;
sc_port<sc_fifo_out_if<YCRCB_frame> > ycrcb_po;
};
//File: YCRCB_Mixer.h
SC_MODULE(YCRCB) {
sc_port<sc_fifo_in_if<float> > K_pi;
sc_port<sc_fifo_in_if<YCRCB_frame> > a_pi, b_pi;
sc_port<sc_fifo_out_if<YCRCB_frame> > y_po;
};
Video_Mixer
Rgb2YCrCb_i
YCRCB_Mixer_i
dvd_in
video_po
control
rgb_pi
ycrcb_po
a_pi
b_pi
y_po
status
K_pi
K
ycrcb_graphics
rgb_graphics

## Slide 27: Example: Video mixer (3)
//File: Video_Mixer.h
SC_MODULE (VIDEO_MIXER) {
// ports
sc_port<sc_fifo_in_if<YCRCB_frame> > dvd_in;
sc_port<sc_fifo_out_if<YCRCB_frame> > video_po;
sc_port<sc_fifo_in_if<MIXER_ctrl> > control;
sc_port<sc_fifo_out_if<MIXER_state> > status;
//local channels
sc_fifo<float> K;
sc_fifo<RGB_frame> rgb_graphics;
sc_fifo<YCRCB_frame> ycrcb_graphics;
// constructor
SC_HAS_PROCESS(VIDEO_MIXER);
VIDEO_MIXER(sc_module_name nm);*
void Mixer_thread();
};
Video_Mixer
Rgb2YCrCb_i
YCRCB_Mixer_i
dvd_in
video_po
control
rgb_pi
ycrcb_po
a_pi
b_pi
y_po
status
K_pi
K
ycrcb_graphics
rgb_graphics
*sc_module_name is the type of the module name (internally managed strings), which must be the 1st parameter if SC_CTOR is not used.

## Slide 28: Example: Video mixer (4)
VIDEO_Mixer::VIDEO_Mixer(sc_module_name nm)
:sc_module(nm)
{
//Instantiate
Rgb2YCrCb Rgb2YCrCb_i("Rgb2YCrCb_i");
YCRCB_Mixer YCRCB_Mixer_i(" YCRCB_Mixer_i ");
//Connect
Rgb2YCrCb_i.rgb_pi(rgb_graphics);
Rgb2YCrCb_i.ycrcb_po(ycrcb_graphics);
YCRCB_Mixer_i.K_pi(K);
YCRCB_Mixer_i.a_pi(dvd_in);
YCRCB_Mixer_i.b_pi(ycrcb_graphics);
YCRCB_Mixer_i.y_po(video_po);
};
Video_Mixer
Rgb2YCrCb_i
YCRCB_Mixer_i
dvd_in
video_po
control
rgb_pi
ycrcb_po
a_pi
b_pi
y_po
status
K_pi
K
ycrcb_graphics
rgb_graphics

## Slide 29: Port arrays
Facility for describing an array of ports.
Can be used, for example, for describing multiplexer inputs.
Syntax:
sc_port <interface[,N]> portname; // N=0..max, default=1 // if N=0, an unlimited number of interfaces may be // connected to the port.

## Slide 30: Example
Switch switch_i
//File Switch.h
SC_MODULE(Switch) { sc_port<sc_fifo_in_if<int>, 4> T1_ip; sc_port<sc_fifo_out_if<int>, 0> req_op; …}
switch_thread
T1_ip
req_op
t1A
t1B
t1C
t1D
req[0]
req[1]
req[2]
req[3]

## Slide 31: Array Connections
// File: board.h #include "Switch.h" SC_MODULE(Board) { const unsigned REQS; Switch switch_i; sc_fifo<int> t1A, t1B, t1C, t1D; sc_signal<bool> req[9]; SC_CTOR(Board): switch_i("switch_i"); {//connect 4 channels to the switch switch_i.T1_ip(t1A); switch_i.T1_ip(t1B); switch_i.T1_ip(t1C); switch_i.T1_ip(t1D); for (unsigned i=0;i!=4;i++) { switch_i.req_op(req[i]); } } };

## Slide 32: Process code
//File: Switch.cpp void Switch::switch_thread() { for (unsigned i=0;i!=req.size();i++) { req[i]->write(true); } //startup after first port is activated wait(T1_ip[0]->data_written_event() //returns reference to event | T1_ip[1]->data_written_event() //that occurs when data is | T1_ip[2]->data_written_event() //written (method of sc_fifo).
| T1_ip[3]->data_written_event() ); for (;;) { for (unsigned i=0; i!=T1_ip.size();i++) { // process each port .. int value = T1_ip[i]->read();… }}}

## Slide 33: Ways to connect (1)
  Channel c1i implements interfaces ifB, ifD,
  channel c2i implements interfaces ifX, ifY,
  channel c3i implements interfaces ifF, if5, ifZ.
  pD is an array port
  mi1 implements an interface ifW ( custom channels, not explained in course)
  processes may communicate with other processes at the same level using channels (see pr2 & pr3)
  pC is of type sc_export (SystemC 2.1: channel moved into module, port can be used like a channel)
pr2
pr1
p1
if1
p6
if6
M1 mi1
pA
pG
pB
pC
ifW
ev1
if2
p2
ifX
ifB
ifD
if3
pE
pD[0]
pD[1]
pF
ifF
pr3
ifZ
ev2
p3
p5
p4
ifY
M2 mi2
Ch3 c3i
Ch2 c2i
Ch1 c1i
ifD

## Slide 34: Ways to connect (2)
  Processes may synchronize with other processes at the same level using event (see pr1 & pr2)
  Processes may communicate upwards in the hierarchy via ports using interfaces (see pr2 & p2).
  Processes may communicate with sub-modules via channels connected to sub-module ports (see pr3 & mi2).
pr2
pr1
p1
if1
p6
if6
M1 mi1
pA
pG
pB
pC
ifW
ev1
if2
p2
ifX
ifB
ifD
if3
pE
pD[0]
pD[1]
pF
ifF
pr3
ifZ
ev2
p3
p5
p4
ifY
M2 mi2
Ch3 c3i
Ch2 c2i
Ch1 c1i
ifD

## Slide 35: Ways to connect (3)
  Processes may communicate with sub-modules by letting the process access the port interface (see pr1 & mi1).
  sc_ports may connect directly to ports of sub-modules (see p1 & mi1)
  port arrays can share the same interface (see pD).
  sc_exports may connect to sc_exports of submodules and channels.
pr2
pr1
p1
if1
p6
if6
M1 mi1
pA
pG
pB
pC
ifW
ev1
if2
p2
ifX
ifB
ifD
if3
pE
pD[0]
pD[1]
pF
ifF
pr3
ifZ
ev2
p3
p5
p4
ifY
M2 mi2
Ch3 c3i
Ch2 c2i
Ch1 c1i
ifD

## Slide 36: Ways to connect (4)
From | To | Method
Port | Sub-module | Direct connect via sc_port
Process | Port | Direct access by process
Sub-module | Sub-module | Local channel connection
Process | Sub-module | Local channel connect or via sc_export or interface implemented by sub-module (hierarchical channel)
Process | Process | Events or local channel
Port | Local channel | Direct connect via sc_export

## Slide 37: Programmable Hierarchy
Feasible to use control structures like for or if then else etc during generation of structures. Example:
varports_i
sc_fifo<int>(D) d2v[0]
sc_fifo<int>(D) v2d[0]
device_i[0]
xmt_p
rcv_p
rcv_p
xmt_p
sc_fifo<int>(D) d2v[1]
sc_fifo<int>(D) v2d[1]
device_i[1]
xmt_p
rcv_p
rcv_p
xmt_p
sc_fifo<int>(D) d2v[N]
sc_fifo<int>(D) v2d[N]
device_i[N]
xmt_p
rcv_p
rcv_p
xmt_p
….
….

## Slide 38: Configura-ble code
#include <systemc.h> #include "varports.h" #include "device.h" int sc_main(int argc, char* argv[]) { // get N from cmd line .. varports* varports_i; device* device_i[N]; sc_fifo<int>* v2d[N]; sc_fifo<int>* d2v[N]; varports_i = new varports(…init parameters…); for (unsigned i=0; i<N; i++) { sc_string nm; nm = sc_string::to_string("device_name_i[%d]",i); device_i[i] = new device(nm.c_str()); nm = sc_string::to_string("v2d[%d]",i); v2d[i] = new sc_fifo<int>(nm.c_str(),fifo_depth); nm = sc_string::to_string("d2v[%d]",i);
d2v[i] = new sc_fifo<int>(nm.c_str(),fifo_depth); device_i[i]->rcv_p(*v2d[i]); device_i[i]->xmt_p(*d2v[i]); varports_i->rcv_p(*d2v[i]); varports_i->xmt_p(*v2d[i]); }

## Slide 39: Summary
  Ports
  Interfaces
  Ports and static sensivity
  pos and neg methods
  LFSR example
  Connecting ports
  Video mixer example
  Port arrays
  Ways to connect
  Programmable hierarchy