## Slide 1: Dynamic processes, testbenches, & modelling styles
P. Marwedel*
Informatik 12, U. Dortmund
* Partially using slides prepared by Tatjana Stankovic from the University of Nis (Serbia and Montenegro), visiting the University of Dortmund under the TEMPUS program.
These slides contain Microsoft cliparts. All usage restrictions apply.

## Slide 2: Dynamic processes (SystemC 2.1)
Functions and methods can be used as dynamic processes.
Prerequisite: #define SC_INCLUDE_DYNAMIC_PROCESSES
Functions that can be used as processes:
void inject(); //ordinary fct w/o args or return value int count_changes(sc_signal<int>& sig)//ordinary fct bool TestChan::Track(sc_signal<packet>& pkt); //method bool TestChan::Errors(int maxwarn, int maxerr); //method

## Slide 3: Syntax for creating dynamic processes
Registration of Dynamic Processes without return value
sc_process_handle hname = sc_spawn ( /* void*/ sc_bind(&funcName, ARGS), processName, SpawnOptions );
sc_process_handle hname = sc_spawn( /*void*/ sc_bind(&methName, object, ARGS) processName, SpawnOptions );
reference to calling module, e.g. this
stack size, don’t_initialize, sensivity
default: call by value

## Slide 4: Debugging and signal tracing
SystemC has no built-in viewer for trace files
(disadvantage if compared to VHDL).
Recommended to generate VCD (value dump format) files.
Waveform interchange format (WIF) also supported.
sc_tracefile* tracefile;
tracefile = sc_create_vcd_trace_file(tracefile_name);
if (!tracefile) cout << "There was an error" << endl;
…
sc_trace(tracefile, signal_name, "signal_name");
…
sc_start();
…
sc_close_vcd_trace_file(tracefile);

## Slide 5: Debugging and signal tracing (2)
  Signal name must be declared before calling sc_trace.
  Hierarchical notation for signals in submodules is feasible.
  Variables, signals and ports can be traced.
  No explicit filename extensions.
  Tracing can be included in constructors of modules

## Slide 6: Debugging and signal tracing: Example
//file wave.h SC_MODULE(wave) { sc_signal<bool> brake; sc_trace_file* tracefile double temperature; };
//file wave.cpp wave::wave(sc_module_name nm);// constructor
:module(nm) { …
tracefile = sc_create_vcd_file("wave");
sc_trace(tracefile, brake,"brake");
sc_trace(tracefile,temperature,"temperature");
}// endconstructor
wave::~wave() {
sc_close_vcd_file(tracefile);
cout << "created wave.vcd" << endl;
}

## Slide 7: Sample output

## Slide 8: Typical TestBench
The stimulus module will provide stimulus to the Device Under Test (DUT) and the Results Checking module will look at the device output and verify the results are correct.

## Slide 9: TestBenches
TestBenches are used to provide stimulus to a design under test and check design results
The testbench can be implemented in a number of ways.
The stimulus can be:
  generated by one process and results checked by another.
  embedded in the main program and results checked in another process.
The checking can be:
  embedded in the main program, etc.
There is no clear "right" way to do a testbench, it is dependent on the user application.

## Slide 10: Typical TestBench
The stimulus module can be implemented by reading stimulus from a file, or as an SC_THREAD process, or an SC_CTHREAD process.
The same is true of the results checking module.
Some designers combine the stimulus and results checking modules into one module.
Also the results checking module can be left out if the designer does manual analysis of the output results.

## Slide 11: TestBench Example: Finite State Machine
Mealy State Machine: has one sequential element -the state vector - and two combinational elements, the output logic and the next state logic.

## Slide 12: TestBench Example: Finite State Machine
A state diagram that represents an example state machine, where a and b represent the outputs.

## Slide 13: TestBench Example: Finite State Machine

## Slide 14: TestBench Example: Finite State Machine
// ** main.cpp
// run forever
SystemC 1.1?

## Slide 15: TestBench Example: Finite State Machine
// ** fsm.h
Old style SystemC

## Slide 16: TestBench Example: Finite State Machine
// ** fsm.cpp

## Slide 17: TestBench Example: Finite State Machine
stimulus.h
Old style SystemC

## Slide 18: TestBench Example: Finite State Machine
stimulus.cpp

## Slide 19: TestBench Example: Finite State Machine
display.h
Old style SystemC

## Slide 20: TestBench Example: Finite State Machine
display.cpp

## Slide 21: Possible SystemC Design Flow

## Slide 22: Possible SystemC Design Flow (2)
Single specification should be partitioned into HW- & SW-parts. HW & SW-submodels should be generated.

## Slide 23: Transaction level modeling
Models in other HW-description languages typically comprise clocking, and simulation is said to be cycle-true, referring to clock cycles of circuits described at the register-transfer level (RTL).
The gas station example does not use any clocks, it is based on the communication of events.
Such models are called transaction-level models (TLM).
TLM models typically simulate significantly faster than RTL models, due to the abstraction used.
Consequently, industry is moving towards TLM for complex circuits.

## Slide 24: Functional Modeling &TLM
Untimed functional models: used to describe & analyze DSP functionality such as filters, decoders, or demodulators.
Effective model of computation: dataflow modeling.
Timed functional models:
  required if either modeling temporal relationships needed to analyze the system behavior
  or if the functional model used as placeholder for its to-be-designed implementation.
Introducing time into untimed functional models can be done by adding wait(sc_time) statements

## Slide 25: Untimed Functional Model
  Design is specified in terms of its functional components
  Functional components specify possible structural boundaries of final implementation
  Some functional components might be merged while other might become discrete cores

## Slide 26: Untimed Functional Model
Dataflow MoC is the most common form of specification
  Alternatively Kahn process networks, Multi-rate dataflow
  Communication between components is through directed point-to-point FIFO
  FIFO are bounded
  Blocking read, blocking write
  Time delays might exist in the model at the boundaries
  Processes in which the model interacts with the environment
  Time delays denote constraints for the system

## Slide 27: Functional Modeling - Example

## Slide 28: Functional Modeling - Example

## Slide 29: Timed Functional Model - Example

## Slide 30: Register-transfer level modeling
"Register-transfer level“: synchronous transfer between functional units, such as multipliers and ALUs, and register files, synchronized by a clock.
  For processors, functional units, register files, and the connection between them are called data-path.
  Transfers in data-path are coordinated by a controller.

## Slide 31: Register-transfer level modeling (2)
Characterized by the kind of channels, ports, and processes
RTL describes cycle-by-cycle behavior
 channels restricted to plain and resolved signals, no complex temporal behavior.
Only port types sc_in, sc_out, and sc_inout (corresponding to sc_signal‘s interfaces), and resolved port types.
Each RTL process is captured by an SC_METHOD.

## Slide 32: General structure of an RTL module
  1 RTL processes  module.
  Process  typical RT component.
  All sequential components are clocked.
  Communication is via signals (intern.) or ports (extern.).

## Slide 33: Modeling levels: classification according to Gajski (Codes/ISSS 2003)
more accurate
Communication
Functionality
untimed
cycle-
accurate
approximately timed
untimed
approximately timed
cycle-
accurate
more accurate
RTL
SAM
TLM
TLM
TLM
TLM
Possible design trajectories
Actually 4 different classes of transaction level modeling (TLM) 

## Slide 34: Classification according to Gajski (Codes/ISSS 2003)
Model | Communication | Functionality
SAM (system architectural model) | UT | UT
Component assembly | UT | AT
Bus arbitration | AT | AT
Bus functional | CT | AT
Cycle accurate computation | AT | CT
RTL | CT | CT

## Slide 35: Advantages and limitations of SystemC
Pros:
  Enables focus on modeling (essential for CS) at a high level.
  Enables development of wrappers around standard algorithms described in C (mpeg, gsm, …)
  Enables path from C to HW, replacing vendor-specific languages from Celoxica (Handel-C) or from CoWare.
  Avoids development of interfaces between HW & SW simulators (such as VHDL/C links).
  High simulation speed is possible with TLM models.
  Full power of OO programming available for HW design.
  Standard libraries such as STL or Boost can be used.

## Slide 36: "Seamless" interface to middleware and OS
e.g.: OS is included in MPARM SystemC-based multi-processor simulation framework from U. Bologna (Benini et al.)
(U. Torino)

## Slide 37: Advantages and limitations of SystemC
First synthesis tools from SystemC start to exist:
  Cynthesizer (http://www.forteds.com/products/cynthesizer.asp)
  Agility (http://www.celoxica.com/products/agility/default.asp)

## Slide 38: Advantages and limitations of SystemC
Cons:
  Mature synthesis technology?
  Semantics definition simulation-oriented.
  Several restrictions due to being based on C++, e.g.
    Event finders
    Varying syntax for structural descriptions
    Resolution functions difficult to use.
    Error reporting, …
  Difficult to use for a hardware engineer.

## Slide 39: Timeline development of SystemC
Date | Version | Notes
Sept 1999 | 0.9 | First version; cycle-based
Feb 2000 | 0.91 | Bug fixes
March 2000 | 1.0 | Widely accessed major release
Oct 2000 | 1.01 | Bug fixes
Feb 2001 | 1.2 | Various improvements
Aug 2001 | 2.0 | Add channels & events; cleaner syntax
Apr 2002 | 2.01 | Bug fixes; widely used
June 2003 | 2.01 | LRM in review
Spring 2004 | 2.1 | LRM submitted for IEEE standard
Dec. 2005 | 2.1 | SystemC accepted as IEEE Standard 1666-2005
June 2006 | 2.2 | Draft & proof of concept
June 2006 |  | Synthesizable subset

## Slide 40: SystemC contrasted with other design languages
Verilog
VHDL
SystemVerilog
matlab
Vera e Sugar Jeda

## Slide 41: Conclusion
  Dynamic processes
  Test benches
  Modeling styles
    transaction level modeling
    untimed model
    timed model
    RTL model
  Evaluation and comparison of SystemC